# Text boxes

Utilities

Storage Room

R | Pitched roof

Ceiling structure and lining

Bathroom

External wall structure

Waste disposal

Paint to doors

Base cabinets

Sink waste

Drainage and pipework

Cabling

Ceiling structure and lining

External wall structure and lining

Mesh reinforcement

Foundations and substructure

Ceiling preparation and finishes

Decoration

Internal doors

Floor preparation

Wired appliances

Bedroom (3)

Floor preparation and finishes

Heating and cooling

Paint to walls

Ceiling preparation and finishes

External windows and doors

Paint to doors

Internal wall preparation

Sink waste

Bath tap

Internal doors and frames

Task

Terms and conditions

Client Supplied

Task

Task

Task

Task

Paint to ceiling

Sockets

Mastic / Sealant

Wired appliances

Decoration

External windows and doors

Steel and structural supports

Material

Material

Specification

Specification

Material

Material

Specification

Specification

Task

Specification

Specification

Professional estimating service

Roof structure and coverings

Specification

QUOTE (quote version 2.28)

Specification

Specification

Specification

Specification

Specification

Specification

Finishes Schedule

Specification

Steel and structural supports

Material

Specification

Specification

Specification

Specification

Preliminaries

Overview

£466.75

Qty

Qty

Qty

£632.61

£424.00

£183.78

Price (£)

Price (£)

£922.04

Qty

Qty

Qty

£16,926.13

Qty

£17,065.60

Qty

£2.93

£1,382.41

£483.67

£618.40

Qty

Qty

£559.20

£427.20

Price (£)

Qty

£632.61

£259.58

Qty

Builder Supplied

Qty

Qty

Qty

Material

£2.93

Price (£)

Price (£)

Some users will want to employ our professional estimating service(s), where schedulers, estimators and/or quantity

Qty

Qty

Qty

Sockets

£160.30

£23.43

Floor finishes

Ceiling lining

Labour

Labour

Labour

Labour

Heating/cooling element

Paint to ceiling

Labour

£80.15

Labour

Labour

Foundations

Labour

Labour

Labour

Ceiling preparation

Areas

£13,120.11

Sockets

Ceiling preparation

Internal doors

External wall structure

Labour

Labour

Labour

Price (£)

Labour

01/12/2022

surveyors provide takeoff, specification and pricing services. The terms for which are as follows:

Sundry items

Labour

Sundry items

Labour

Task

Labour

Ceiling lining

Paint to skirting

Hot and cold pipework

Labour

Specification

Materials

Materials

Material

Materials

Specification

Materials

Specification

perimeter

Specification

Specification

Materials

Materials

Page 47 of 48

Protection

1. Definitions and Interpretation

Coat Hook/Towel Hook

Materials

Free standing sink tap and mixer

Materials

Specification

Materials

Materials

Skip

Materials

Specification

Specification

Specification

Specification

Materials

Materials

Specification

Specification

Lintels

Materials

Lintels

Materials

Specification

Specification

Materials

Bathroom

Specification

Materials

Bargeboards

Specification

Materials

Wet underfloor heating - 5m2 kit

Qty

Mid spec (Grohe PC Supply £270)

Price (£)

Qty

Qty

Qty

£13,473.30

Qty

Qty

Total

300mm height

Total

Qty

Qty

Total

Total

Total

12 yard skip

Specification

Total

Total

Qty

Specification

Total

Brushed stainless steel round coat hooks (£12/each PC allowance)

Specification

Total

Qty

Total

Total

Qty

Qty

Total

Qty

Example new build

LoPro®Max OneZone® underfloor heating - 5m2 kit

1.1 In these Terms and Conditions, unless the context otherwise requires, the following expressions have the following

Total

Qty

Total

Qty

Total

Total

Specification

Total

Qty

Total

Labour

Mist coat and two coats of

100mm Concrete block wall;

Labour

Qty

Mesh reinforcement to slab in G |

Labour

Labour

Labour

Base cabinet in Kitchen / Living /

Qty

Bedroom

Labour

Powered by BuildPartner

meanings: "Agreement" means the contract into which you and we will enter if you accept our Proposal. The Agreement will

31.68

Plasterboard to external wall (inner

Qty

859.20

Decoupling membrane to walls in

356.40

Labour

Labour

Labour

Labour

Qty

Labour

Labour

Electrical wiring installation in G |

Sink waste in Kitchen / Living /

Primer, undercoat and gloss coat

Labour

960.00

Mist coat and two coats of paint to

Labour

Single softwood door, frame,

Labour

Delivery and collection of portaloo

Primer, undercoat and gloss coat

Labour

Materials

Materials

architrave, handle and lock in

Materials

Labour

Mastic / sealant in WC

Materials

Materials

Materials

to softwood door in Kitchen /

Materials

Materials

Skip in Middle Floor

Labour

Shaver socket in WC

Sink waste in Bathroom

Materials

Materials

Materials

Materials

Flooring underlay in Bedroom (3)

Materials

Materials

Labour

£5,085.28

Materials

Bath tap in Bathroom

Labour

Materials

incorporate, and be subject to, these Terms and Conditions; "Consumer" means a consumer as defined by the Consumer

150mm ready mix C25 concrete slab

Mid spec (Victoria Plum)

Mid spec (PC Supply £30

Materials

Dining room

Total

Total

Allowance for WCs

Materials

Total

Total

Total

Total

walls in Bedroom

external wall in Middle Floor

Total

Dining room

in G | Ground Floor

eggshell paint to ceiling in WC

Mid spec (The Bath Store)

to softwood door in Bathroom

Skip

Materials

Total

Total

12 yard skip

Total

150mm concrete slab

Ground Floor

Ground Floor

Total

Total

Materials

Fullsize dishwasher

Total

Total

Concrete padstone

Wet underfloor heating per m2

leaf)

Rights Act 2015; "Client" means you, the party accepting our estimate or Proposal or placing an order with us. Where an

Bedroom (2)

Bathroom

Total

Mid spec (Wickes Wood

Total

Hot and cold pipes; copper in

1,188.00

Schlüter®-DITRA 25

Mid spec (Samsung or similar, PC Supply £490)

A142 mesh reinforcement

Double power socket in Storage

Mid spec (Dulux or similar

Cavity tray weep ends (2nr

New wiring allowance

Primer, undercoat and gloss coat

Single softwood door, frame,

Double panel radiator in Bedroom

Mid spec (Dulux or similar

Skim to ceiling in Kitchen / Living /

12.5mm standard gyproc plasterboard

Single plasterboard to ceiling in

£5,094.09

inpidual is entering into this Agreement on behalf of a business, the inpidual confirms they have the authority to enter into this

Mid spec (Howdens)

Fibre Underlay or similar

each)

Damp Proof Course / DPC in G |

100mm concrete blocks;

Mid spec (Victoria Plum)

1 unit

12 yard skip

Mid spec (Dulux or similar

Single plasterboard to ceiling in G |

Boiler Cupboard

2 unit

Portaloo delivery

Mist coat and two coats of paint to

Living / Dining room

215x215x102mm

1item

Total

150mm ready mix C25 concrete

Total

1 unit

Total

Double power socket in Bedroom

Cavity tray weep ends (2nr

Pro-Warm wet underfloor heating kit and thermostat

Total

56m

Rigid protection to floor in

600mm wide by 1000mm deep

Skim to ceiling in Bedroom

48.00

Bedroom (3)

approved)

£0.00

matting

architrave, handle and lock in

approved)

Agreement on behalf of that business and the business will be the Client in the context of this Agreement; "Project" means

allowance) per structural opening

allowance) per structural opening

1point

approved)

Carpet to floor in Bedroom (2)

stretcher bond; 1:3 mortar;

1 unit

8.349999 unit

£20.00

303.00

1,920.00

403.20

Mid spec (Direct Doors)

1 unit

£10.00

646.80

45m²

approved); white

£0.00

Mid spec (Dulux or similar

Dining room

Middle Floor

(3)

2.16m²

15.75m²

the development project as detailed in our Proposal, in relation to which we are to render our Services; "Proposal" means the

7N

£732.71

approved)

£274.80

1 unit

£0.00

Ground Floor

1 unit

£6,424.01

£960.00

ceiling in Boiler Cupboard

£422.19

Ground Floor

Room

(2)

Kitchen / Living / Dining room

Bargeboard in R | Pitched roof

3mm thistle multi-finish

£10.00

Mid spec (PC Sum £45/m2)

9.6m²

Single steel lintel in Storage Room

to skirting in Storage Room

£60.00

£103.64

£60.31

slab in G | Ground Floor

£36.00

38.4m²

Single steel lintel in Bedroom (3)

£40.99

£648.00

Mid spec (PC Supply £220

Mid spec (Dulux or similar

22mm copper

12.5mm standard gyproc

1 unit

in WC

Mid spec (Dulux or similar

£490.44

15.75m²

£112.00

£960.00

Bathroom

Mid spec (PC Supply £9/m)

in Bedroom

£37.80

Catnic CG90/100

Mid spec (Hamilton, PC

3mm thistle multi-finish

150mm concrete slab

£60.00

12.5mm standard gyproc

£36.00

£102.59

Catnic CG90/100

£49.61

15.75m²

Boiler Cupboard

75.6m²

DPC; 300mm width

£5,010.00

£28.94

£66.00

Mid spec (Hamilton, PC

Wet underfloor heating per m2

£294.80

Bathroom

Plasterboard to stud wall - inner leaf

Concrete padstone

£112.56

£46.00

Skirting

proposal we give to you in accordance with clause 2 detailing the Services we will provide to you and the fees we will charge;

Fuseboard

trench foundations (4-10m run)

£312.00

40m²

Bath waste

£107.71

12.5mm standard gyproc plasterboard

plasterboard

1m

Toilet

£14.40

£248.06

£463.18

Mid spec (Direct Doors)

£66.00

£2,873.65

Supply £25 each)

Cavity tray; weep ends (2nr

£44.79

£46.00

£5,742.71

£7.70

Mid spec (Wickes or similar approved)

28m

£63.13

£1,155.50

"Services" means the Services we will provide as specified in the Agreement or otherwise agreed between the Parties; and

plasterboard

£98.11

12-module fuseboard

each)

13m

Cavity tray; weep ends (2nr

45m²

215x215x102mm

£751.64

approved); white

Supply £25 each)

Shuttering, concrete and mesh

£164.88

approved)

£102.59

Floor structure and lining

2m

Pro-Warm wet underfloor heating kit and thermostat

8m

Corex

Wired appliances

6m

£2,052.09

1 unit

allowance)

Fuseboards

£36.64

Floor structure and lining

75.60

£200.00

1point

41.04

£850.50

Wired appliances

96.00

£424.00

Portaloo weekly hire in G | Ground

G | Ground Floor

Specification

6m²

1 unit

£14.40

0.81m²

Ceiling preparation and finishes

Wall cabinets

Specification

£54.44

£27.22

£116.99

£310.92

allowance)

45m²

121.20

£18.90

£94.41

4point

5,779.20

45m²

2,688.00

£220.27

£418.75

£117.25

"Site" means the site at which construction is to take place for the Project.

£553.57

£125.21

£48.00

£115.20

£60.31

Paint to walls

£649.58

£3,297.60

£105.86

£452.25

£452.25

£10.85

£183.78

£64.07

£241.25

£154.44

1 unit

£150.00

Paint to doors

£3,207.59

1.2 Each reference in these Terms and Conditions to:

Specification

£9.74

Decoration

£16.59

1 unit

£112.00

£52.93

Qty

Paint to architraves

£63,408.10

£1,098.56

Specification

Primer, undercoat and gloss coat to

£1,188.00

Drainage and pipework

Qty

£116.99

Paint to architraves

£3,474.63

£1,498.92

Specification

Skim to walls in Bathroom

Wall preparation and finishes

£7.20

Kitchen / Living / Dining room

Window board

£315.20

Labour

£466.75

Labour

£2.09

£2,235.52

Qty

Floor

£312.00

Floor lining

Specification

£80.15

£279.65

Qty

£126.99

£33.00

£6.84

Skirting

£132.00

1.2.1 "we", "us" and "our" means the Company and includes all employees, agents and sub-contractors of ours;

£180.36

£160.30

£2.09

Damp Proof Course / DPC

Acrylic shower tray (~1-2m2)

£180.36

Ventilation

Specification

£277.20

Fused spur

£1.33

£25.20

Labour

DPC; 300mm width

£373.25

Qty

£632.61

Wall ties in Middle Floor

Wall preparation and finishes

Specification

£1,134.54

skirting

External windows and doors

External windows and doors

£0.84

£29,102.39

Roof lining

Materials

Qty

1.2.2 "you" and "your" means the Client;

100mm Concrete block wall;

Waste pipework

Mid spec (PC Supply £15 each)

Specification

600mm wide by 1000mm deep

Floor insulation

£427.20

£0.84

Mid spec (Victoria Plum or similar, PC Supply £150)

£12.19

£71.27

£23.43

Ceiling preparation

Specification

Timber window board

£93.31

Qty

Skirting in Bedroom (2)

£632.61

Sockets

Mid spec (Wickes or similar approved)

Portaloo

£424.00

3mm thistle multi-finish

Labour

£35.46

Materials

Ceiling lights

Labour

15.84

Specification

24m²

6week

Qty

79.20

Wired appliances

Paint to walls

Paint to windows

Qty

Ceiling lights

Hot and cold pipework

Total

109.44

Mid spec (Wickes or similar

Qty

Stainless steel wall ties;

Materials

Paint to skirting

Middle Floor

9.74

£2.93

Mid spec (Dulux or similar approved)

Drainage and pipework

Specification

Specification

£448.08

Specification

£2.93

trench foundations (4-10m run) in

Labour

1.2.3 "writing" and "written" includes emails;

Materials

Labour

Drainage and pipework

Total

Steel and structural supports

Drainage and pipework

198.00

Specification

Materials

Labour

Specification

Qty

£38,388.56

£0.00

Qty

external wall in G | Ground Floor

£1,341.66

Materials

Total

Internal doors and frames

Qty

approved)

Total

Specification

76-100mm cavity; 4nr/m2

Specification

Specification

Labour

£109.28

Materials

Specification

Internal doors and frames

7.20

Labour

Qty

Qty

£251.25

1.2.4 a statute or provision of a statute is a reference to that statute or provision as amended or re-enacted at the relevant

Internal wall preparation

£1,427.69

Specification

Sundry items

Wall cabinet in Kitchen / Living /

Total

Sundry items

Total

Internal wall finishes

Labour

Labour

Labour

Bath waste in Bathroom

Materials

time;

£28.80

100mm concrete blocks;

Labour

Qty

Labour

Materials

Specification

£922.04

£259.20

R | Pitched roof

Gas combi boiler

Primer, undercoat and gloss coat to

£139.80

G | Ground Floor

Qty

£4,051.51

£80.15

Pedestal toilet in WC

Additional works

75.6m²

£885.60

Total

Damp proof membrane / DPM

16m

Skirting

Qty

Qty

Materials

Qty

Wood sheathing to roof

Qty

Shuttering, concrete and

£13,120.11

£424.00

Allowance for any other works required not identified in schedule

Materials

Total

Materials

Labour

Hot and cold pipework

Lintels

Total

Access points

£269.09

£80.00

Hot and cold pipework

Fuseboard in G | Ground Floor

Labour

Labour

18mm Structural Hardwood Plywood Sheet

Labour

Primer, undercoat and gloss coat

Materials

Mid spec (Wickes or similar approved)

Specification

£280.05

Qty

Labour

Sockets

Worcester Bosch Greenstar 30i Gas/LPG Combi Boiler

£424.00

Labour

Specification

Materials

Mid spec (Victoria Plum or

Total

Materials

Mist coat and two coats of

£259.20

1.2.5 a "Party" or the "Parties" refer to the parties to these Terms and Conditions;

stretcher bond; 1:3 mortar;

Specification

Mid spec (Victoria Plum)

Primer, undercoat and gloss coat

2000 gauge (500mu) DPM

Tile adhesive and grouting to walls

Storage Room

800.28

Labour

Internal doors

Materials

7N

Total

Total

1.2.6 "these Terms and Conditions" is a reference to these Terms and Conditions; and

Total

Professional fees

Materials

1,360.80

Specification

Qty

Materials

Materials

Bathroom extractor fan in

skirting

£109.44

1 unit

Specification

Specification

Internal doors

Total

177.84

Materials

Dining room

Materials

Qty

0.00

£68.95

93.96

mesh

Qty

Total

Primer, undercoat and gloss coat

Specification

Specification

similar, PC Supply £190

12-module fuseboard

Double power socket in Kitchen /

Mid spec (Howdens)

Labour

Materials

Total

Qty

Specification

£189.44

Total

1.2.7 a clause or paragraph is a reference to a clause of these Terms and Conditions.

1 unit

each)

Floor board in Middle Floor

£2,527.15

£338.04

Qty

Total

Labour

Total

to softwood architrave in Bathroom

Mid spec (Dulux or similar approved)

Labour

eggshell paint to walls in WC

Specification

75.6m²

to softwood architrave in Kitchen /

Insulation to concrete slab in G |

Specification

Waste pipe overground in Kitchen

Qty

28m

Qty

Total

£12.50

Breather membrane in R | Pitched

to softwood door in Bedroom

Total

Qty

8.349999 unit

Floor preparation

in Bathroom

Labour

Qty

£1,155.50

£482.50

Labour

Mid spec (Dulux or similar

Primer, undercoat and gloss coat

1 unit

1.3 The headings used in these Terms and Conditions are for convenience only and will have no effect on their interpretation.

Decoupling membrane to floor

£1,407.00

Wooden worktop / Laminate worktop

Bargeboard

Qty

Labour

Hot and cold pipes; copper in

19.20

£65.99

Mid spec (Dulux or similar

Total

Bathroom

Mist coat and two coats of paint to

Materials

18mm Structural Hardwood

Mid spec (Dulux or similar

WC

Materials

Labour

Materials

Skim to ceiling in WC

Qty

Soffit and fascia system

Half brick wide brick wall (100mm

Primer, undercoat and gloss coat

Gas pipes

Labour

Materials

Total

Mid spec (PC Supply £9/m)

Words signifying the singular number will include the plural and vice versa. References to any gender will include the other

Mid spec (PC Supply £80

Total

£2,052.09

approved)

Primer, undercoat and gloss coat to

Downlight in Bedroom (3)

roof

approved)

£5,779.20

3mm thistle multi-finish

Downlight in Storage Room

Mid spec (PC Supply £20/m)

Ground Floor

Mid spec (PC Supply £120/m)

Living / Dining room

10mm flexible adhesive and

Labour

Materials

Plywood Sheet

Materials

£78.49

£647.12

Materials

Total

/ Living / Dining room

Labour

approved)

Living / Dining room

Schlüter®-DITRA 25 matting

£72.50

Labour

Specification

£75.60

Materials

22mm copper

1 unit

Mid spec (Dulux or similar

MAPEI grouting

154.44

Ceramic tiles to walls, excluding

Mid spec (Hamilton, PC

Materials

to skirting in Bedroom (3)

Total

Total

£5,456.60

Total

2.16m²

Boiler Cupboard

Skim to walls in Bedroom

Flush plate

to window board in Storage Room

£3,207.59

£7,186.20

Materials

£3,006.00

110mm UPVC pipe

14.4m²

Qty

792.00

£558.10

475.20

Mid spec (PC Supply £15

45m²

£250.80

Total

172.80

gender. References to persons will include corporations.

Materials

Tyvek Supro breather

120mm Celotex XR4000

each)

Total

wide) in Middle Floor

Mid spec (PC Supply £15

24.24

walls in Boiler Cupboard

1 unit

Labour

Total Cost

Engineering bricks; (100mm wide)

3mm thistle multi-finish

£323.30

Total

£102.59

Total

each)

Hot and cold pipes; copper in

adhesive and grout in Kitchen /

Supply £25 each)

Hot and cold pipes; copper in

Cavity closers in Bedroom (3)

Mid spec (Dulux or similar

£22.61

£30.99

£472.50

skirting

Cavity closers in Storage Room

each)

Page 48 of 48

Kitchen / Living / Dining room

45m²

Mid spec (Dulux or similar

1point

Double power socket in Bedroom

Facing bricks @ PC Sum

£183.92

Brick manhole; 750x450mm;

£3,653.12

22mm copper

Specification

Mid spec (Dulux or similar

membrane

8m

100mm Concrete block wall; external

approved)

Total

9.6m²

£60/m2; stretcher bond; incl.

£615.60

Single steel lintel in Bathroom

0.9m

approved)

Soil pipe overground

Steel and structural supports

£188.44

Mid spec (Dulux or similar approved)

approved); white

half brick wide (inner leaf) in G |

£184,953.24

1 unit

Qty

Worktops

£100.00

Supply & Install Professional

2point

Wall ties in G | Ground Floor

6point

£2.59

Base cabinet

£51.32

£6.00

100mm thick Kingspan

Single softwood door, frame,

4point

Hardcore fill / sub base / sub-base

58.499996m²

£60.30

Single softwood door, frame,

£14.40

Decoupling membrane to floor

£60.31

approved)

Materials

100mm thick Kingspan

38.4m²

31.20

wall

£25.20

Middle Floor

£36.99

£100.80

Ex. VAT

£120.63

1:3 mortar

£30.99

£361.88

16m

Thermabate Cavity Closer

Toilet seat in WC

(2)

Thermabate Cavity Closer

6.4800005m²

Specification

£134.73

1m

Schlüter®-DITRA 25 matting

£1,088.10

Catnic CG90/100

£402.00

Total

Living / Dining room

architrave, handle and lock in

cleaning on project completion in

Bathroom

£116.99

£1,435.86

1000mm depth in G | Ground Floor

£22.50

£144.00

Labour

Stainless steel wall ties;

£241.25

Soil pipe

£17.28

250mm MOT type 1 hardcore

£235.24

Mid spec (Howdens)

Brick manhole;

Ground Floor

£77.58

£46.08

Toilet seat (PC Supply £25

54.00

Floor structure

22mm copper

Page 2 of 48

£1,624.30

£12.96

£244.00

£75.60

75.6m²

Mid spec (Hamilton, PC

£400.75

Wall preparation and finishes

£6.00

£66.00

£170.85

£82.76

4m

Primer, undercoat and gloss coat to

£161.11

1m

100mm concrete blocks; stretcher bond; 1:3 mortar; 7N

1,552.50

architrave, handle and lock in WC

Qty

22mm copper

£113.40

Fixtures and fittings

76-100mm cavity; 4nr/m2

Mid spec (PC Sum £60/m2)

Paint to architraves

6m

£7.54

£70.20

67.32

Materials

5,010.00

Paint to windows

Labour

£41.04

£10.65

£35.46

Perimeter insulation / Insulation to

Heating and cooling

Total

Supply £25 each)

75.6m²

£316.85

£475.28

£19.20

£186.63

Mid spec (Direct Doors)

6m²

Soil pipe underground, trench by

each)

£3,798.90

Specification

Lintels

750x450mm; 1000mm

Tile backer board to walls in

2m

£36.99

Flooring underlay in Bedroom (2)

£61.56

9m

Class B Engineering bricks;

Bedroom

G | Ground Floor

£1.20

£204.93

2,052.09

£448.08

£27.22

Specification

Ceiling lights

Specification

Qty

Specification

Qty

£50.00

Mid spec (Wickes Wood

Switches

Decoupling membrane to walls

£175.87

£269.09

Mid spec (Direct Doors)

1item

£52.93

Heating and cooling

Hardwood casement window (0-1m2)

Qty

£225.00

Floor preparation and finishes

£6,332.26

stretcher bond; incl. 1:3

Specification

Materials

Middle Floor

£395.28

4point

£93.41

window board

£32.40

£8.74

£48.60

£168.03

Bath

1item

£190.05

Switches

1 unit

Ceiling lights

depth; incl. excavation; 150

Flush plate in Bathroom

Preliminaries

Mid spec (Slim Line or similar approved, PC Supply £600 each)

machine

Schlüter®-DITRA 25 matting

mortar

Qty

£12.50

Double panel radiator

Specification

£475.20

Specification

£3,688.00

£112.00

£241.25

£28.80

Labour

Total

Paint to doors

Primer, undercoat and gloss coat

Bathroom

£590.00

Qty

concrete bed; 215 class B

Specification

1 unit

Labour

Mid spec (Victoria Plum)

Fibre Underlay or similar

Timber battens in R | Pitched roof

£68.95

£10,131.16

Mid spec (Dulux or similar approved)

£80.15

Furniture, fixtures &

£73.44

£110.16

perimeter in G | Ground Floor

£129.60

Paint to ceiling

Internal wall preparation

Labour

£354.60

External wall structure and lining

equipment

Heating/cooling element

38x38mm timber battens

382.80

Qty

Qty

engineering brick walls; 100

Schluter KERDI BOARD

8.400001m²

Wall insulation

Specification

Mid spec (PC Supply £220 each)

Labour

1.20

Window furniture

£132.00

£33.00

Mid spec (Grohe PC Supply

Specification

Specification

Qty

Labour

Materials

£338.04

£651.07

£0.00

£78.80

£112.00

Materials

Windows

107.71

£312.00

25mm thick Kingspan

£1,382.41

Wooden worktop / Laminate

110mm uPVC pipe with gravel fill

£2,069.55

approved)

Materials

804.00

Internal wall preparation

£373.25

Labour

Specification

£590.00

518.40

Half brick wide brick wall (100mm

£85)

Waste pipework

Total

Total

Qty

Specification

£422.10

£9,884.35

Specification

clayware main channel;

£424.00

Labour

58.499996m²

to window in Storage Room

Specification

Floor finishes

worktop in Kitchen / Living / Dining

277.20

£45.50

15.75m²

Materials

Labour

Specification

Heat source

Total

£312.00

Waste pipework

Ridge tiles; butt jointed; bedding and

Tile Backer Board 12.5mm

Materials

Kooltherm K103 Floorboard

Qty

Qty

£1,295.25

to perimeter; n.e. 300mm

Bath tap

£263.25

Total

General allowances

Materials

Qty

concrete benching; step

Primer, undercoat and gloss coat

Project management

Labour

Specification

Mid spec (Dulux or similar

£424.00

Primer, undercoat and gloss coat

Qty

Total

Specification

Specification

Materials

pointing in natural coloured mortar

Drainage and pipework

Qty

Specification

Delivery and collection of excavator

Labour

1 unit

Qty

Sink waste

£300.38

Materials

Ceiling lights

Labour

Hardwood casement window (1-2m2)

£49.61

Qty

9.6m²

Timber floor structure in Middle

Specification

room

Labour

Qty

Specification

Labour

Materials

Labour

Qty

Mid spec (Slim Line or similar approved, PC Supply £790 each)

height

approved)

Specification

Total

£44.79

Total

£722.48

Specification

Labour

Specification

Labour

Wall insulation

wide) in G | Ground Floor

irons and cast iron manhole

Qty

Qty

Total

Materials

Mid spec (The Bath Store)

£150.75

Heating and cooling

£25.00

£421.20

Engineered wood to floor

Single steel lintel in Kitchen /

Excavator

Qty

Materials

Steel beam

Materials

£94.41

to softwood architrave in Bedroom

Downlight in Bathroom

1,044.00

Floor

to window board in WC

Labour

203x203x86 UC

Facing bricks @ PC Sum

Labour

Qty

Total

cover

Light switch - 1 gang in Storage

Labour

274.80

Materials

Qty

Materials

Mid spec (PC Sum £60/m2)

Specification

Total

Qty

Total

Materials

Qty

Engineering bricks; (100mm wide)

Downlight in Kitchen / Living /

£112.20

£125.82

Labour

Labour

Mid spec (PC Supply

Materials

28m

Light switch - 1 gang in Bedroom

£555.26

1 unit

(1:3)

£684.45

180.00

Materials

Hot and cold pipework

Materials

half brick wide (outer leaf) in G |

Labour

Mid spec (Dulux or similar

1,351.38

Materials

3,168.00

Total

Total

Mid spec (Dulux or similar

£706.01

£175.88

£427.20

£60/m2; stretcher bond; incl.

Living / Dining room

1 unit

Mist coat and two coats of paint to

Total

Total

Total

Qty

Labour

£120/m)

Labour

£131.91

Materials

Primer, undercoat and gloss coat

Labour

75x200 C24 joists @400

Roof coverings

£137.20

Mid spec (PC Supply £15

Materials

Concrete/cement ridge tile (PC Supply £15/m)

Decoration

£427.13

Heating/cooling element

1:3 mortar

Cavity wall insulation in Middle

Room

5m

Total

Bath waste

approved)

Delivery and collection of portaloo

Skim to walls in WC

Dining room

Materials

cts, struts and hangers

to softwood door in Boiler

Materials

178.20

Catnic CG90/100

Materials

£143.47

Sink taps

Labour

Materials

Specification

Hardwood casement window

approved)

Total

Floor preparation and finishes

(3)

Hot and cold pipes; copper

Wet underfloor heating per m2 in

Total

Total

Coat Hook/Towel Hook in

Total

£14.40

each)

Specification

22mm copper

Total

Waste pipe overground in

Total

Specification

Gas combi boiler in Boiler

Mid spec (Hamilton, PC

75.6m²

£319.35

Skim to walls in Kitchen / Living /

Soil pipe overground in Middle

ceiling in Bedroom (3)

Ground Floor

£1,134.54

Total

Mid spec (PC Supply £15

Materials

Total

3m

Steel column

Specification

Cavity wall insulation

Qty

£146.31

1m

1 unit

£246.25

Mid spec (Victoria Plum)

£679.24

45m²

3mm thistle multi-finish

Mid spec (Hamilton, PC

4point

Portaloo delivery

Window board in Storage Room

Qty

Kitchen / Living / Dining room

50mm Kingspan Kooltherm K108 Cavity Insulation Board

£241.25

Qty

£7.54

Supply £10 each)

Rigid protection to floor

£1,279.07

£1,237.50

66.00

Paint to ceiling

Labour

Bathroom

Labour

Supply £10 each)

£1,106.36

Floor

£30.99

each)

Carpet to floor in Bedroom

£792.00

65.99

Supply & Install Project manager

14.4m²

Total

Cupboard

Paint to skirting

Qty

Floor lining

£3,798.90

203x203x86 UC

£81.66

Class B Engineering bricks;

Mid spec (Dulux or similar

12.96

(1-2m2) in Bedroom (3)

Timber window board

Floor finishes

1point

Mid spec (Slim Line or

1,980.42

£6,332.26

Brushed stainless steel

£75.60

Labour

Materials

50mm Kingspan Kooltherm

Inspection Chamber in G | Ground

£150.75

£972.00

1m

External wall insulation / External

Corex

approved); white

£158.80

Specification

Specification

Labour

£6.00

Sink waste in WC

Bathroom

Mid spec (Dulux or similar

Floor

Additional works in Middle Floor

£1.20

Downlight in Bedroom (2)

Pro-Warm wet underfloor

4point

Dining room

2,918.98

stretcher bond; incl. 1:3

Materials

Specification

£1,038.25

Cupboard

Mid spec (PC Sum £45/m2)

1point

mortar

Total

approved)

£240.45

£36.99

£241.25

£20.00

6.84

£60.31

15.75m²

Soil pipe

Bathroom extractor fan

Qty

Total

round coat hooks (£12/each

Qty

Allowance for any other

Qty

Materials

Mid spec (PC Supply £15

£2,209.50

£17.28

15.75m²

£60.31

£316.85

3mm thistle multi-finish

heating kit and thermostat

110mm UPVC pipe

Hot and cold pipes; copper

Specification

Materials

Design of steel connections

£10,131.16

K108 Cavity Insulation

Decoration

similar approved, PC Supply

Worcester Bosch Greenstar

Mid spec (Victoria Plum)

on site in G | Ground Floor

£8.74

PC allowance)

£75.60

Wall lining

£168.03

£248.06

£15.84

8.400001m²

£211.05

Design of steel connections

1 unit

Board

Primer, undercoat and gloss coat

Cement tiles to roof in R | Pitched

9m

Floor

£13.20

Switches

62.4m²

Total

22mm copper

40m²

£790 each)

£13.20

each)

10day

Labour

Steel and structural supports

Bedroom (2)

Qty

2m

30i Gas/LPG Combi Boiler

Supplier quotation - Glazing

Total

Portaloo weekly hire

1 unit

works required not identified

Mid spec (PC Supply £80 each)

Single steel lintel in Kitchen /

Wall Board in Bathroom

Labour

Labour

£10.00

75.6m²

Polypropylene inspection

£3,150.00

1 unit

£653.25

£850.50

25.92

Steel and structural supports

£73.51

Portaloo

Hot and cold pipes; copper in WC

Materials

Supplier quotation

2 unit

6point

£25.89

£35.84

Materials

£422.10

£73.51

Materials

£25.00

Free standing sink tap and mixer

in schedule

100.80

£202.50

Labour

Scaffolding to elevations (m2)

£1,000.00

£316.85

£2,119.17

Specification

Floor preparation and finishes

1 unit

Specification

240.00

100mm Kingspan Kooltherm

£102.59

Living / Dining room

£36.00

£54.00

£2,688.00

£0.00

£2,311.49

£74.88

£708.75

£187.50

Ceiling preparation and finishes

Qty

Ventilation

Double panel radiator in Bedroom

Simple Scaffold

£36.00

Insulation K15 Rainscreen

to window in WC

chamber

£395.72

Paint to skirting

roof

£14.40

£1,098.56

22mm copper

£236.94

Internal doors and frames

Total

1,000.00

£15.00

£300.38

Qty

Total

Ceiling preparation and finishes

£361.88

1item

259.20

Total

Materials

£256.50

Mid spec (Dulux or similar

Specification

£728.13

Mist coat and two coats of paint to

1.8m

Specification

Design of steel connections

£0.00

£3,688.00

£46.00

Hot and cold pipes; copper

1,542.24

Padstones

Blinding

Catnic CG90/100

£568.33

2 unit

£1,980.42

Mid spec (PC Supply

Timber stud wall / timber partition

£3,150.00

in Bathroom

Board

Labour

Labour

Total

£31.68

Mid spec (PC Supply £220

£160.30

£113.40

£61.00

Primer, undercoat and gloss coat

£722.48

£1,044.00

£1,360.80

£116.99

Paint to walls

Design of steel connections

2m

Screed to floor in G | Ground Floor

£46.68

£2,069.55

24m²

approved)

50mm sand blinding

Ceramic tiles to floor, excluding

£0.00

Specification

£277.21

Materials

22mm copper

Paint to architraves

Materials

Scaffolding

Qty

ceiling and cornice in Storage

Waste pipe overground in Middle

£22/m2)

Qty

£183.78

Weak mix concrete between cavity

£424.00

£475.28

£2,376.14

£23.34

Floor finishes

Plumbed appliances

Lintels

Specification

£45.00

Skirting in Bedroom

Tile adhesive and grouting to walls

Sink

each)

£1,231.50

Mid spec (Grohe PC Supply

Tile adhesive and grouting to floor

wall; 600mm centres; 3 rows of

Heating and cooling

Internal doors and frames

below DPC / Lean mix concrete

Screed to floor

Qty

Internal wall structure and lining

480.00

Specification

Ceiling preparation

Mid spec (Wickes or similar

28.80

£25.92

1 unit

58.499996m²

Total

10mm flexible adhesive and MAPEI grouting

to skirting in Bedroom (2)

Specification

Labour

£324.00

Total

Labour

243.00

£270)

Internal doors

Specification

1 unit

£251.25

Specification

£0.00

Switches

65mm screed

£54.44

Ceiling preparation and finishes

Qty

Ceiling preparation

Specification

£845.27

Qty

Specification

Specification

between cavity below DPC in G |

£601.21

Room

£1,752.95

£70.92

approved)

Qty

£150.00

£1,044.00

Qty

£105.86

adhesive and grout in Bathroom

45m²

Toilet brush in Bathroom

£131.91

Boxing to pipework / beam / column

Labour

Specification

Floor

Professional fees

Plasterboard to external wall (inner

£1,592.30

noggins

Qty

in Kitchen / Living / Dining room

Materials

3.89

Qty

65mm screed

Labour

Materials

Mid spec (Dulux or similar

Specification

1 unit

10mm flexible adhesive and

Materials

Labour

£160.30

Qty

£9.45

Specification

£320.34

Mid spec (PC Supply £40

Labour

Labour

Total

£14.40

Sink taps

Qty

Timber stud wall; C16/C24 47x95mm; 600mm centres; 3 rows of

£40.00

Qty

Labour

Total

approved)

Mid spec (Dulux or similar

£1,698.84

Materials

Heating/cooling element

£424.00

Waste pipework

16m

110mm UPVC pipe

Qty

Labour

£277.20

£3,395.91

Hot and cold pipework

982.80

Light switch - 1 gang in Bathroom

Hot and cold pipes; copper

Mid spec (PC Sum £60/m2)

Double power socket

£1,295.25

£982.80

Specification

External windows and doors

6m²

noggins

Total

22mm copper

Specification

16m

Specification

approved); white

MAPEI grouting

Ceiling preparation

Specification

£80.00

Mid spec (Hamilton, PC Supply £25 each)

Materials

Internal doors

9m

leaf) in G | Ground Floor

Labour

£3,291.14

Total

£427.20

Internal wall structure

Ductwork and associated BWIC

External windows and doors

Materials

Labour

Materials

Ground Floor

Materials

£356.40

(floor to ceiling)

Qty

Mid spec (Hamilton, PC

Materials

each)

Tile adhesive and grouting to floor

Primer, undercoat and gloss coat

Labour

£146.31

Labour

Total

Supply £10 each)

Timber stud structure with MR plasterboard

Qty

Paint to doors

Total

£109.44

Materials

Specification

allowance in Kitchen / Living /

Qty

£112.50

to skirting in Kitchen / Living /

Ridge tiles; butt jointed; bedding

Wired appliances

Materials

Qty

12.5mm standard gyproc

Materials

£396.40

Mist coat and two coats of paint to

2m²

444.89

Specification

Weak mix concrete between

10mm flexible adhesive and MAPEI grouting

Specification

1 unit

Labour

6m²

£170.85

£1,303.14

Self levelling compound to floor

Total

Total

115.20

£175.87

33.00

Qty

Materials

Total

£189.44

£2,014.84

Qty

Total

Labour

Total

and pointing in natural coloured

Total

Labour

1point

Labour

Labour

£19.20

cavity below DPC; 100mm

£27.22

Total

Qty

£37.69

Vapour barrier

Qty

10.80

Ceramic tiles to floor, excluding

3-5mm Latex Levelling Screed / Latex Floor Levelling Compound

Materials

plasterboard

Shower mixer and head

Scaffolding to elevations (m2) in G

£475.20

Specification

£58.68

Concrete padstone in Middle Floor

£162.00

85.54

Primer, undercoat and gloss coat

£7.50

Windows

£190.05

£651.07

Labour

Specification

215x215x102mm

£10.80

6.43

Specification

£3.29

walls in Bedroom (3)

Qty

Total

£52.80

to softwood architrave in Boiler

Single steel lintel in Bedroom (2)

thick cavity; 500mm height

£60.31

£922.04

Labour

Materials

Boxing to pipework / beam / column

Double power socket

£274.50

Wall hung sink in WC

Floor preparation

75.6m²

Wall ties

Materials

Hot and cold pipes; copper

Light switch - 1 gang in Bedroom

Materials

Sundry items

Single softwood door, frame,

Dining room

Dining room

Labour

Materials

£13.20

architrave, handle and lock in

Specification

Qty

Mid spec (Dulux or similar

Ductwork and associated

Materials

Heating and cooling

£443.20

Stainless steel wall ties; 76-100mm cavity; 4nr/m2

Skim to ceiling in Bedroom (3)

Materials

mortar (1:3) in R | Pitched roof

Paint to ceiling

22mm copper

allowance

Mid spec (Dulux or similar

2 unit

£48.49

Materials

Supply & Install Professional

| Ground Floor

Tile adhesive and grouting to walls

£30.51

Mid spec (Hamilton, PC Supply £25 each)

Specification

£60.30

Total

Catnic CG90/100

Total

Tile adhesive and grouting to floor

Qty

Labour

Total

Skim to ceiling in Storage Room

Specification

adhesive and grout in WC

Mid spec (The Bath Store,

Sockets

Total

Labour

PC Supply £140)

68.95

Paint to walls

Specification

£56.11

Free standing sink tap and mixer

£303.00

Materials

approved); white

BWIC allowance

Qty

Specification

3mm thistle multi-finish

Hot and cold pipes; copper in G |

Mid spec (PC Sum £60/m2)

Qty

Concrete/cement ridge tile

Total

129.60

Qty

Simple Scaffold

Total

3mm thistle multi-finish

Total

(length of room)

10mm flexible adhesive and MAPEI grouting

(2)

Shaver socket

28m

Floor preparation and finishes

cleaning on project completion in

£73.51

approved)

Labour

Cupboard

2m

66.00

15.75m²

Waste pipe overground in WC

Labour

26m

75.6m²

Storage Room

Electric towel rail in Bathroom

£48.00

Boxing to pipework / beam /

Mid spec (PC Supply £30 each)

Single softwood door, frame,

in Bathroom

Materials

Mid spec (Dulux or similar

1item

£598.05

Mid spec (Hamilton, PC

£175.88

1 unit

Timber stud structure with MR plasterboard

£746.21

Qty

Sockets

Specification

£54.44

Total

Labour

Materials

Qty

38.4m²

Labour

10.80

(PC Supply £15/m)

2.16m²

2m²

Toilet roll holder in Bathroom

Mid spec (PC Supply £160

Materials

Mid spec (PC Supply £40

Labour

10mm flexible adhesive and

£490.44

Middle Floor

£5,535.60

£63.32

Insulation between studs

Total

£104.11

Skim to ceiling in Boiler Cupboard

37.80

Total

£164.88

column (floor to ceiling) in Middle

Materials

Double power socket

£0.00

Mid spec (Direct Doors)

£20.94

110mm UPVC pipe

Inset mirror

Primer, undercoat and gloss coat

9m

£105.86

Wall insulation

£258.72

Labour

Materials

approved)

in Kitchen / Living / Dining room

Qty

£41.88

Supply £10 each)

architrave, handle and lock in

Specification

285.12

£112.50

Ground Floor

Pipework

£277.63

1point

Supporting steel

Labour

Specification

£434.60

each)

1item

Mid spec (Hamilton, PC Supply £25 each)

£160.30

MAPEI grouting

£31.20

Total

3mm thistle multi-finish

£2.40

Vapour control layer to floor in G |

£171.07

1 unit

Floor preparation

Tile adhesive and grouting to walls

£176.40

Specification

1 unit

£18.90

Qty

Materials

£1,542.24

each)

1.8m

Mid spec (PC Supply £150 each)

22mm copper

100mm Rockwool RWA45 Semi-Rigid Acoustic Insulation Slab

Integrated shower mixer and head

£99.87

Mid spec (Grohe PC Supply

£120.00

Boxing to pipework / beam / column

Total

Total

£63.13

Materials

Floor

£308.83

Qty

10mm flexible adhesive and MAPEI grouting

£30.99

0.81m²

to softwood door in WC

£1,542.24

6m²

£590.00

Bedroom (3)

235.87

1 unit

External windows and doors

Sand blinding

£183.78

£270)

£288.90

Qty

Materials

198.00

1 unit

Total

9m

£161.88

£22.50

£178.20

Total

£23.34

£234.39

Shower screen

Labour

Hardwood casement window

Specification

132.00

£60.31

Specification

£112.00

£553.57

Cavity tray over structural opening

£312.00

£13.20

Paint to windows

Total

Flooring underlay in Bedroom

Materials

£6.00

Mid spec (Dulux or similar

Wall preparation and finishes

Labour

Tile adhesive and grouting to floor

£8.48

£0.00

Half brick wide brick wall (100mm

17.28

£90.47

Qty

Paint to doors

Mid spec (Victoria Plum)

in Bathroom

Mist coat and two coats of paint to

£7.50

Timber stud structure with

Wall preparation and finishes

£37.69

Sink taps

Labour

Mid spec (Direct Doors)

(width of room)

£32.40

£278.07

£225.00

Site set up

Specification

Qty

Vented extractor fan / cooker hood

Ground Floor

1 unit

in Kitchen / Living / Dining room

£52.80

£590.00

Total

Inspection Chamber

Roof insulation

1 unit

190.80

Specification

Double power socket in Bedroom

£73.51

Mid spec (Victoria Plum, PC

Materials

£424.00

Downlight

£129.60

Vapour barrier type 230

£10.80

Timber stud structure with MR plasterboard

Labour

Labour

approved)

£36.99

Specification

Qty

Mist coat and two coats of paint to

Specification

£201.60

MR plasterboard

£11.74

£0.97

Mid spec (Wickes Wood

£54.90

Specification

(0-1m2) in Bathroom

£40.00

Materials

Materials

£356.40

Heating and cooling

£292.07

Mid spec (PC Supply £15 each)

in Kitchen / Living / Dining room

1 unit

2.7m

£354.60

Manthorpe Horizontal Cavity

158.40

Sundry items

in WC

45m²

Qty

£48.49

wide)

Qty

Materials

G | Ground Floor

Tile backer board to walls

Total

£168.03

£448.08

Mid spec (Hamilton, PC

Supply £280)

Labour

Qty

£112.00

Ceiling preparation and finishes

Qty

Heating and cooling

Total

£9.45

Project management

Polypropylene inspection chamber

Fibre Underlay or similar

Mid spec (Slim Line or

Specification

£60.30

ceiling in Bedroom (2)

£396.40

£102.59

Wall preparation and finishes

Supply £25 each)

Total

Materials

10mm flexible adhesive and

£103.64

Specification

Tray

walls in Storage Room

Mirror

approved)

Specification

Labour

Internal wall preparation

Schluter KERDI BOARD Tile Backer Board 12.5mm

324.00

Shaver socket in Bathroom

Wet underfloor heating per m2 in

Qty

Internal wall preparation

75.60

Labour

Facing bricks @ PC Sum £60/m2; stretcher bond; incl. 1:3 mortar

Waste pipework

Shower waste (acrylic tray)

Mid spec (Dulux or similar

£94.50

Total

Labour

Preliminaries

Mid spec (Bosch PC Sum

Cavity wall insulation in G |

£312.00

Labour

similar approved, PC Supply

1 unit

£62.50

555.26

Flooring underlay in Kitchen /

£1,276.27

4point

Gas pipes in Middle Floor

£14.40

Specification

15.75m²

Specification

Materials

Qty

Mid spec (Dulux or similar

6,332.26

£85.54

£600 each)

Dishwasher

Materials

Specification

Design of steel connections in

Specification

5m

£124.20

approved); white

Total

Breather membrane

MAPEI grouting

Tile skirting to floor in Bathroom

Labour

Mid spec (PC Supply £30

Qty

£475.33

£220/nr)

Materials

£183.78

Mid spec (Victoria Plum)

Materials

£424.00

Qty

1point

Total

15.75m²

£180.04

22mm copper

Labour

Qty

Materials

Pipework

Ceiling preparation

Heating and cooling

£75.61

each)

£20.94

Labour

Insulation to concrete slab

Qty

2.16m²

29.99

Downlight

£227.84

£369.60

Total

£241.25

Qty

Bathroom

Mid Spec (PC Sum £18/m)

£49.61

Total

Total

£116.99

£11,292.34

Ground Floor

Specification

Heating/cooling element

1 unit

approved); white

Tyvek Supro breather membrane

10m

Internal wall preparation

70.20

Mid spec (PC Supply £15 each)

Middle Floor

£211.05

Labour

Total

1point

120mm Celotex XR4000

18m

£432.10

Tile skirting to floor

Pro-Warm wet underfloor

Primer, undercoat and gloss coat

Labour

Boxing to pipework / beam /

Plasterboard to stud wall - outer leaf

£175.00

Primer, undercoat and gloss coat

50mm Kingspan Kooltherm

Labour

Labour

£44.79

Specification

Materials

Specification

Specification

£37.74

Living / Dining room

Materials

Blinding in G | Ground Floor

£13.57

Steel and structural supports

Wall mounted sink tap and mixer

14.4m²

£132.00

General allowances

Paint to architraves

Qty

£60.31

Mid Spec (PC Sum £18/m)

heating kit and thermostat

Qty

£427.20

Materials

Materials

column (length of room) in Middle

Total

K108 Cavity Insulation

£94.41

12.5mm standard gyproc plasterboard

£804.00

£183.92

Labour

£60.31

£209.38

Specification

Brick manhole; 750x450mm;

Materials

£25.89

£3.89

Insulation to roof between rafters

50mm sand blinding

113.40

£373.25

£58.68

1,435.86

Qty

Qty

Single plasterboard to ceiling

Mastic / Sealant

£290.40

£425.25

Materials

Specification

Design of steel connections

Total

Mid spec (Wickes Wood

to window board in Kitchen / Living

Specification

Site set up in G | Ground Floor

45m²

Qty

Labour

to softwood door in Bedroom (3)

Labour

£37.80

Total

Cavity tray over structural opening

Fibre Underlay or similar

Materials

Ductwork and associated BWIC

Site set up, portaloos,

£350.71

4 unit

£236.94

12.5mm standard gyproc plasterboard

Specification

144.00

Heating/cooling element

£172.80

6m²

Total

Board

121.20

£23.67

£4,929.65

£17.46

Internal doors and frames

Supply & Install Project manager

Total

Qty

Qty

in WC

Ceiling lights

£240.00

£979.00

Labour

Decoration

Total

£598.05

Soil pipe underground, trench by

Hob

Qty

/ Dining room

approved)

Total

Specification

180.36

£150.00

£207.59

Padstones

Labour

Mist coat and two coats of paint to

Specification

1000mm depth

Insulation to roof between rafters

Materials

Labour

Materials

Materials

£188.44

Mid spec (Dulux or similar

£449.38

in R | Pitched roof

temporary electrical and

Mid spec (Grohe PC Supply

£0.00

Labour

Paint to walls

£98.11

75.6m²

Supplier quotation - Glazing in

Floor

£403.20

£243.00

Total

Total

£270)

£395.72

140mm Kingspan Thermaroof TR26 Flat Roof Insulation Board

Ceiling preparation and finishes

approved)

on site in Middle Floor

40m²

Mid spec (Dulux or similar

Skim to walls in Storage Room

allowance

Qty

in Bedroom (2)

Skim to walls in Bedroom (3)

Wiring and fuseboards

Qty

£424.00

Tile skirting to floor

Inset mirror in Bathroom

Labour

Specification

140mm Kingspan

Single softwood door, frame,

Materials

Specification

Specification

£240.00

Tile skirting to floor in WC

plumbing, hoardings,

Timber stud structure with

Materials

Paint to doors

Floor preparation

Materials

Total

Fullsize dishwasher in Kitchen /

£1,134.54

Brick manhole; 750x450mm; 1000mm depth; incl. excavation; 150

concrete bed; 215 class B engineering brick walls; 100 clayware

£240.00

MR plasterboard

office/canteen etc.

Mid Spec (PC Sum £18/m)

Paint to skirting

Specification

£431.44

Total

Labour

Qty

Qty

Manthorpe Horizontal Cavity

£1,980.42

Thermaroof TR26 Flat Roof

Qty

Materials

Mid spec (PC Supply £150

ceiling

approved)

Internal doors

Mid Spec (PC Sum £18/m)

Total

Labour

Specification

10day

£553.20

2,263.14

Ductwork and associated BWIC allowance

1 unit

Bathroom (Subcontract)

Total

£126.00

machine in G | Ground Floor

1 unit

3mm thistle multi-finish

3mm thistle multi-finish

First Fix Pipework in Storage

Supplier quotation

Intumescent paint to steel beam in

14.4m²

£113.76

Living / Dining room

Labour

Total

120.00

Primer, undercoat and gloss coat

Materials

Additional works in G | Ground

Tray

240.00

Electric towel rail in WC

Qty

Skim to ceiling in Bedroom (2)

Damp proofing

110mm uPVC pipe with

Specification

1 unit

9m

£40.00

Insulation Board

Qty

main channel; concrete benching; step irons and cast iron manhole

£3,150.00

Labour

Specification

£70.01

architrave, handle and lock

each)

£102.59

6m

1m

£583.81

£2,376.14

Plumbed appliances

Materials

Labour

Mid spec (Dulux or similar approved); white

38.4m²

Labour

£356.40

45m²

gravel fill

Total

3mm thistle multi-finish

Materials

Qty

£150.75

Skim to walls in Boiler Cupboard

Ceiling preparation

Qty

Materials

£315.00

£125.63

Mid spec (Samsung or

£0.00

£402.00

£239.76

Room

Labour

1m

Mid spec (Direct Doors)

Electrical certification

Specification

Total

1 unit

Internal wall structure and lining

cover

Materials

1item

Mid spec (PC Supply £160

Integrated shower mixer and head

1.33

£0.00

£14.40

£7.54

Floor

Labour

to softwood architrave in WC

Specification

£0.00

Total

Specification

18m

Materials

First fix pipework

679.24

Total

Qty

Mist coat and two coats of paint to

312.00

Mid spec (Victoria Plum, PC Supply £280)

£285.12

similar, PC Supply £490)

Materials

£4.19

£46.08

£3,128.12

3mm thistle multi-finish

Timber battens

Labour

£2,400.00

£144.00

Floor finishes

£116.99

Mastic / sealant in Bathroom

each)

£396.40

Middle Floor

£17.28

£1.20

£30.00

£3,150.00

Total

Double panel radiator in Bedroom

£423.98

15.75m²

Electric hob

Electric hob in Kitchen / Living /

Allowance for any other

£198.00

1 unit

Materials

Paint to architraves

£168.03

Downlight in Bedroom

£1,000.00

Specification

38x38mm timber battens

1 unit

£2,400.00

£448.08

£269.63

Allowance for bathrooms,

Qty

6.4800005m²

Materials

Mid spec (PC Supply £240 each)

£2,263.14

£1,196.44

£3,395.91

Intumescent paint

Qty

1item

Mist coat and two coats of paint to

£8.74

£164.88

Wired appliances

Total

Supply & Install Working foreman

£600.12

Concrete padstone in G | Ground

Mid spec (Dulux or similar

369.60

Shower tray

£7.55

Total

Labour

Waste disposal

£50.00

Specification

Mid spec (PC Supply £15

(3)

Qty

Floor preparation

£1,000.00

Specification

Floor preparation and finishes

£18.90

Materials

£11.74

£35.00

302.40

Labour

approved)

Floor preparation and finishes

£2,687.12

5m

Boxing to pipework / beam /

Single steel lintel

Carpet to floor

Labour

ensuites and kitchens

Primer, undercoat and gloss coat

Total

£90.47

£518.40

Total

£67.84

Internal wall structure

Primer, undercoat and gloss coat

Decoupling membrane to floor in

£228.00

works required not identified

ceiling

421.20

Flashing

in schedule

in Middle Floor

Bedroom

Materials

£1,714.84

Mid spec (PC Supply £220

£13.13

Dining room

Mid spec (Dulux or similar approved); white

Intumecent paint to steel column

column (width of room) in Middle

Specification

to window in Kitchen / Living /

Primer, undercoat and gloss coat

Specification

Materials

£201.60

£7.78

Mid spec (PC Sum £45/m2)

£183.78

£104.69

£649.58

Floor

Single softwood door, frame,

Catnic CG90/100

£646.80

walls in Bedroom (2)

Specification

Total

each)

Qty

Internal doors and frames

1item

Window furniture

Qty

Labour

1 unit

Wall preparation and finishes

£1,382.41

£144.95

850.50

Qty

Mid spec (PC Supply £240

£292.07

£0.00

Damp proof membrane / DPM in G

Materials

£696.80

each)

Qty

Intumescent paint

Mid spec (Dulux or similar

1item

architrave, handle and lock in

£75.61

Timber floor structure

6point

215x215x102mm

Total

£30.99

Waste pipe overground in G |

Specification

52.93

Qty

Labour

£48.13

Total

Specification

Ventilation

£29.22

10day

Bathroom

25.89

Steel and structural supports

Labour

to softwood door in Storage Room

Electric oven

£424.00

£0.00

Mist coat and two coats of paint to

£361.88

Mid spec (Dulux or similar

Schlüter®-DITRA 25

Labour

Sink

Qty

75x200 C24 joists @400 cts, struts and hangers

Labour

to skirting in Bedroom

Total

Wet underfloor heating - 5m2 kit in

Floor preparation

Floor finishes

Mid spec (Belling)

£2,099.87

Labour

Heating/cooling element

each)

Qty

£133.91

Materials

Materials

1 unit

£6.00

Floor

Page 17 of 48

Dining room

Specification

approved); white

63.12

4 unit

Supply & Install Electrical

£120.00

972.00

Cavity closers

Specification

Materials

1point

Materials

Labour

£36.99

Timber stud structure with

Internal doors

Total

Total

Labour

£160.30

£112.23

Materials

38.4m²

approved)

Specification

Single steel lintel

Specification

£120.00

£113.40

Skim to ceiling in Bathroom

Mid spec (Dulux or similar

£0.00

matting

Kitchen / Living / Dining room

Ground Floor

£448.08

£0.00

Mid spec (Dulux or similar

| Ground Floor

Skirting in Kitchen / Living / Dining

298.80

Specification

£150.00

Qty

MR plasterboard

Qty

Lintels

£96.00

Steel beam in Middle Floor

Acrylic shower tray (~1-2m2) in

2000 gauge (500mu) DPM

Materials

Materials

£0.00

6m²

£277.20

£490.44

1 unit

Catnic CG90/100

ceiling

Total

Mid spec (Direct Doors)

Qty

Intumescent paint to steel beam

£475.28

Sink

3mm thistle multi-finish

certification in Middle Floor

approved)

100mm thick Kingspan Thermabate Cavity Closer

Total

Fixtures and fittings

£2,099.87

£60.31

WC

Internal wall preparation

Qty

Total

approved)

Specification

Primer, undercoat and gloss coat

110mm UPVC pipe

Qty

Labour

£102.59

Switches

16m

1 unit

£302.40

Specification

room

32.40

Timber hoarding

105.86

LoPro®Max OneZone®

1 unit

£62.81

Specification

5m

203x203x86 UC

Machinery / Equipment

9m

Total

Specification

Labour

45m²

Total

Intumescent paint

Boxing to pipework / beam /

Labour

Qty

Scaffolding

£63.13

£208.23

Decoupling membrane to floor in

1 unit

Materials

Labour

£427.20

Mid spec (Dulux or similar approved); white

Electric towel rail

to softwood architrave in Bedroom

Labour

6m²

£131.91

£112.50

Skip in G | Ground Floor

Labour

underfloor heating - 5m2 kit

Materials

Bathroom

Specification

£175.00

£395.28

Qty

Total

£362.71

£120.63

Mid spec (PC Supply £160 each)

£170.85

£62.81

Page 14 of 48

Qty

Materials

Specification

£112.00

Specification

65.76

£553.57

£14.40

OSB hoarding with built in door and timber lock, plm (max 2.8m

Materials

Mid spec (Wickes or similar

5m

£67.32

Materials

column (floor to ceiling) in G |

Supporting steel

29.22

Qty

£103.64

approved)

Window board in Bathroom

(3)

201.60

£158.40

£93.96

Qty

12 yard skip

Oven

£14.40

£482.09

Furniture, fixtures &

Total

Single steel lintel

Specification

Lead flashing in R | Pitched roof

£19.20

WC

high)

Labour

Total

£130.13

Mid spec (Victoria Plum or

Qty

£116.99

Paint to doors

£312.00

Mist coat and two coats of paint to

Labour

Total

£7.20

£0.00

£162.00

Labour

Materials

1item

Total

Cavity closers

Qty

Decoration

Schlüter®-DITRA 25

Labour

Bathroom extractor fan in WC

£424.00

26m

Labour

equipment

Materials

£125.00

4 unit

Qty

£146.31

similar, PC Supply £150)

100mm thick Kingspan Thermabate Cavity Closer

Double panel radiator in Storage

Specification

Kitchen sink

Ground Floor

Mid spec (Dulux or similar

Labour

£274.50

Specification

£120.63

Total

Kitchen sink in Kitchen / Living /

92.40

£70.01

Paint to architraves

Catnic CG90/100

£333.40

Materials

Lead Code 4 - 300mm

£197.60

Materials

Timber window board

£1,351.38

£190.05

Self levelling compound to floor in

Wall preparation and finishes

Total

Specification

Qty

£0.00

approved)

Roofing Lead Flashing Roll

Single softwood door, frame,

£1,833.47

Excavation for substructure

Cabling

1m

Plasterboard to stud wall - inner

Page 24 of 48

Undermount stainless steel kitchen sink (Grohe)

ceiling and cornice

Electrical wiring installation

£130.00

Carpet to floor in Bedroom (3)

Wiring and fuseboards

Qty

£859.20

48.60

Timber stud structure with

158.80

Materials

Paint to ceiling

1 unit

Total

Paint to ceiling

Total

Mid spec (PC Supply £80

matting

Materials

Specification

Materials

Labour

Specification

£984.20

External wall structure and lining

Specification

Qty

Labour

Total

Specification

Labour

£20.00

each)

2.16m²

Dining room

Mid spec (PC Sum £45/m2)

Total

Room

Materials

Qty

420.00

Timber pitched roof structure

architrave, handle and lock in

Total

£177.84

£1,920.00

Specification

£95.00

Storage Room

New wiring allowance

£802.87

Mid spec (Dulux or similar approved); white

1 unit

MR plasterboard

14m

£1,920.00

Mid spec (PC Supply £220

£117.25

£30.99

Delivery and collection of

Scaffolding to elevations (m2) in

Sink waste

Total

3.29

Single steel lintel in Bedroom

Pedestal sink in Bathroom

Materials

Qty

leaf in Middle Floor

Undermount stainless steel

£2,325.63

Labour

75x145mm sawn treated timber

15.75m²

£198.00

1point

Cavity tray over structural opening

Plumbed appliances

Qty

2.7m

Qty

£22.61

£1,141.91

£15.84

Qty

Skim to walls in Bedroom (2)

40.99

Materials

Paint to ceiling

3-5mm Latex Levelling

£307.84

Labour

12.5mm standard gyproc

£35.84

£24.24

Total

£94.50

£16,799.14

Engineered wood to floor in

Catnic CG90/100

£293.00

1,188.00

Labour

£246.96

Mid spec (Victoria Plum)

kitchen sink (Grohe)

Mist coat and two coats of paint to

Lead flashing

Manthorpe Horizontal Cavity Tray

£60.31

each)

3mm thistle multi-finish

£6.00

Internal wall finishes

Labour

Materials

Engineering bricks; (100mm wide)

Materials

Light switch - 1 gang in Bedroom

Bedroom (2)

Specification

Screed / Latex Floor

Labour

Mid spec (Victoria Plum)

Electrical certification

Labour

Total

£248.06

Design of steel connections in G |

Hoarding

1 unit

£46.85

Mid spec (Hamilton, PC

Wall lining

Materials

Total

Mid spec (Direct Doors)

Specification

Materials

Middle Floor

£850.50

£85.54

Specification

Page 3 of 48

plasterboard

7.55

excavator in G | Ground Floor

Materials

£1,160.10

38.4m²

Specification

£364.21

36.00

1 unit

Lead Code 4 - 300mm Roofing Lead Flashing Roll

Levelling Compound

Bath

£100.80

1 unit

2m

£36.99

Electric oven in Kitchen / Living /

Primer, undercoat and gloss coat

Total

Qty

Materials

Specification

£73.75

246.96

Total

Qty

Kitchen / Living / Dining room

Excavator

£180.04

Qty

Toilet brush

walls

half brick wide (inner leaf)

Labour

Ground Floor

Primer, undercoat and gloss coat

30.24m²

£150.00

£402.00

Boiler Cupboard

£1,098.56

£73.75

£161.11

2m²

Fascias

1 unit

Qty

Supply £10 each)

£54.44

Total

Simple Scaffold

Page 37 of 48

Specification

Total

Total

Decoration

£83.99

Coat Hook/Towel Hook in WC

Specification

Site set up

Electrical wiring installation in

Design of steel connections

Ceiling lights

to softwood door in Bedroom (2)

Dining room

Qty

Qty

£112.00

Excavate for substructure by

75.6m²

Labour

Mist coat and two coats of paint to

Cavity tray over structural opening

to softwood architrave in Storage

Labour

1point

£277.20

Materials

£8.38

Class B Engineering bricks; stretcher bond; incl. 1:3 mortar

£420.00

Mist coat and two coats of paint to

Internal doors and frames

£46.08

£105.86

Boxing to pipework / beam /

Labour

£177.28

Mid spec (Dulux or similar approved); white

1 unit

Mid spec (PC Sum £60/m2)

Mid spec (PC Supply £40 each)

Site set up, portaloos, temporary electrical and plumbing,

£60.31

£160.30

Qty

£157.74

Materials

£312.00

Brushed stainless steel

Mid spec (Dulux or similar

£121.20

Total

Labour

£6.43

300.38

Light switch - 1 gang

10.65

£427.20

Skirting in Bedroom (3)

£448.08

£493.75

ceiling in Kitchen / Living / Dining

Materials

52.80

machine; not exceeding 1m depth;

8 unit

£580.91

£0.00

£0.00

Mid spec (Belling)

column (length of room) in G |

Materials

Labour

Specification

40m²

Manthorpe Horizontal Cavity Tray

Engineering bricks; (100mm wide)

Materials

Mastic / Sealant

£13.20

Page 39 of 48

Total

£180.00

disposal by hand n.e. 25m to

Room

£424.00

Page 8 of 48

37.74

£1,542.24

Mid spec (Wickes or similar

£14.81

ceiling in Bedroom

Mist coat and two coats of

£0.00

Total

Total

£1,820.00

£424.00

Labour

£298.48

round coat hooks (£12/each

Qty

hoardings, office/canteen etc.

Toilet

approved)

Materials

Mid spec (Hamilton, PC Supply £10 each)

Page 12 of 48

Middle Floor

Page 34 of 48

Mist coat and two coats of paint to

1point

£90.47

2,400.00

Timber stud wall / timber partition

£180.00

New wiring allowance

£73.51

Mid spec (Dulux or similar

Total

Toilet roll holder

skip/across site in G | Ground

Labour

Ceramic tiles to walls, excluding

Cavity tray weep ends (2nr

£1,542.24

1 unit

Mid spec (Dulux or similar

Total

Supply & Install Electrical

£3,168.00

Ground Floor

Materials

Page 16 of 48

13.20

Specification

eggshell paint to ceiling in

Floor finishes

Specification

room

£480.00

PC allowance)

Timber hoarding in G | Ground

approved)

Page 11 of 48

Mid spec (PC Supply £40 each)

£298.80

walls

56m

Mid spec (Dulux or similar

half brick wide (outer leaf)

Timber stud structure with

Scaffolding to elevations (m2) in

approved)

wall; 600mm centres; 3 rows of

Qty

Total

Plasterboard to external wall (inner

£4,988.00

£480.00

Specification

Qty

£102.59

approved); white

16m

2 unit

Materials

Page 9 of 48

Intumecent paint to steel column in

Units and worktops

£389.27

certification in G | Ground Floor

Bath in Bathroom

Qty

Bathroom

£14.40

Class B Engineering bricks; stretcher bond; incl. 1:3 mortar

allowance) per structural opening

Skim to ceiling

Total

approved); white

Soffit and fascia system in R |

£15.00

Labour

Labour

Light switch - 1 gang

£422.19

£80.00

Excavator in G | Ground Floor

adhesive and grout in Bathroom

Floor

Floor

1 unit

Mid spec (Dulux or similar approved); white

15.75m²

MR plasterboard

52.80

300.38

Middle Floor

Mid spec (PC Sum £60/m2)

Mid spec (Dulux or similar

Labour

40m²

Material removed from site

Materials

£30.99

Switches

£109.44

1.5T excavator; incl.

OSB hoarding with built in

23.67

leaf) in Middle Floor

noggins in Middle Floor

9m

£40.99

Mid spec (Hamilton, PC Supply £10 each)

Mid spec (Victoria Plum)

£116.99

3mm thistle multi-finish

£31.68

Materials

Cavity tray; weep ends (2nr allowance)

1 unit

£211.05

£120.63

0.97

£315.00

Downlight in WC

Timber stud wall; C16/C24

door and timber lock, plm

Paint to architraves

Simple Scaffold

1 unit

0.84

Materials

£463.18

Specification

approved)

Excavate for substructure by

Toilet seat

Mist coat and two coats of paint to

to skips

£10,434.08

£536.00

Total

26.40

£189.44

insurance + fuel allowance

Total

£6.00

12.5mm standard gyproc

£46.68

Pitched roof

G | Ground Floor

£25.89

9.6m²

Total

£285.12

1week

£236.94

Specification

Intumescent paint

Toilet seat (PC Supply £25 each)

machine; not exceeding 1m depth;

Qty

Page 32 of 48

Page 27 of 48

£87.50

45m³

Mid spec (PC Supply £15

Mid spec (PC Supply

Mastic / sealant in Kitchen / Living

£65.76

47x95mm; 600mm centres;

75.6m²

plasterboard

(max 2.8m high)

£281.40

£0.00

£36.99

Page 15 of 48

6m²

WC

33.00

£601.76

Page 10 of 48

walls

disposal by hand n.e. 25m to

Labour

£0.00

each)

3 rows of noggins

£382.80

Qty

Pedestal toilet in Bathroom

Skim to ceiling

7m

Cement tiles to roof

£760.32

10.8m

£20/m)

Toilet brush in WC

Mastic / sealant

£1,978.59

£0.00

£600.12

£120.63

£80.40

75.6m²

£0.00

£21.38

£330.00

£470.30

£1,041.72

£226.13

18m

Labour

Steel and structural supports

Paint to walls

4point

Mid spec (PC Supply £22/m2)

30.24m²

Skirting in Storage Room

£234.50

3mm thistle multi-finish

Page 23 of 48

Materials

Allowance for bathrooms, ensuites and kitchens

Mid spec (Victoria Plum or

£1,542.24

/ Dining room

£443.20

Mid spec (PC Supply £40

Mid spec (Dulux or similar approved); white

Boxing to pipework / beam /

Allowance for bathrooms,

Vapour control layer to floor

Mid spec (Wickes or similar

each)

£330.00

1,698.84

Specification

£719.71

120.00

similar, PC Supply £190

£303.00

£63.12

£565.31

£1,978.59

Page 6 of 48

column (width of room) in G |

2.40

Total

£92.40

63.13

£101.78

£1,542.24

£241.25

Page 4 of 48

Materials

skip/across site

Page 29 of 48

each)

1 unit

Fused spur in Kitchen / Living /

Paint to walls

ensuites and kitchens

Material removed from site to skips

£80.15

Vapour barrier type 230

£444.89

Excavation for foundations

£326.90

Qty

£746.21

Total

£289.24

Mist coat and two coats of paint to

£475.20

Ceramic tiles to floor, excluding

£75.60

approved)

£7.50

Ground Floor

£1,040.51

124.20

£1,164.60

Skim to ceiling

Specification

1item

Demolitions

Materials lift in G | Ground Floor

£316.85

Page 30 of 48

Mastic / sealant

Primer, undercoat and gloss coat

1 unit

0.00

Intumescent paint to steel beam in

Labour

6m

Specification

Lintels

Allowance for WCs

walls

Qty

£72.50

Insulation between studs in Middle

adhesive and grout

Specification

Geni SLA15 363kg

Roof structure

£52.80

£30.00

Materials

3mm thistle multi-finish

Dining room

Qty

Switches

Timber stud structure with

to softwood architrave in Bedroom

Excavate for trench foundations by

£0.00

MR plasterboard

Qty

£41.04

Specification

60.00

Specification

Labour

2.59

£120.00

£497.81

Labour

Vented extractor fan / cooker hood

£60.30

Mid spec (PC Supply £15

Mid spec (PC Sum £60/m2)

Mid spec (Dulux or similar approved); white

£250.80

Total

2week

G | Ground Floor

machine; not exceeding 1m depth;

102.59

£71.04

£0.00

Mid spec (Bosch PC Sum £220/nr)

Light demolition

each)

Materials

Labour

Qty

171.07

Mist coat and two coats of paint to

Floor

disposal by hand n.e. 25m to

£323.30

£120.00

Materials

(2)

Qty

5m

Intumescent paint

Labour

£528.00

walls in Kitchen / Living / Dining

Skim to ceiling

100mm Rockwool RWA45

Specification

5m

4point

Materials

Page 25 of 48

Labour

Toilet roll holder in WC

Ceramic tiles to floor, excluding

£175.00

Materials lift

Mid spec (Dulux or similar

Total

Total

290.40

Primer, undercoat and gloss coat to

Excavate for trench foundations by

£104.69

Vinyl flooring in Storage Room

skip/across site

Materials

Mid spec (PC Supply £40

£241.25

Semi-Rigid Acoustic

approved)

Toilet seat in Bathroom

£528.00

Materials

Geni SLA15 363kg

£158.40

Mist coat and two coats of

Qty

3mm thistle multi-finish

Total

Total

Insulation Slab

Material removed from site to skips

Vinyl flooring (PC Sum

Total

Page 18 of 48

£79.20

adhesive and grout

£333.40

1 unit

Labour

7.20

Vinyl flooring

each)

softwood door

room

528.00

£29.22

Toilet seat (PC Supply £25

machine; not exceeding 1m depth;

Mid spec (Dulux or similar approved)

£30.99

disposal by hand n.e. 25m to

£20/m2)

0.00

£320.45

Timber pitched roof structure in R |

Mid spec (PC Sum £60/m2)

Single steel lintel in WC

each)

1 unit

Materials

eggshell paint to walls in Bathroom

Vinyl flooring (PC Sum £20/m2)

£133.91

Mid spec (Dulux or similar

Plasterboard to stud wall - inner

30.24m²

Mid spec (Dulux or similar

1item

475.20

£284.92

Skim to ceiling

52.80

approved); white

Light switch - 1 gang in WC

Total

£6.00

£7.50

Mesh reinforcement to slab

Light switch - 1 gang in Kitchen /

skip/across site in G | Ground

2m²

Supply & Install Steel beam in G |

Catnic CG90/100

14.40

£6.30

Clear site of bushes, scrub and

£52.80

A142 mesh reinforcement

Excavator

Primer, undercoat and gloss coat to

£36.99

3mm thistle multi-finish

1m

leaf in G | Ground Floor

£12.50

62.4m²

Pitched roof

approved)

Ceramic tiles to walls, excluding

£235.87

Mid spec (Hamilton, PC

Page 13 of 48

£33.00

24m²

Floor

Living / Dining room

£520.79

Ground Floor

75x145mm sawn treated

£52.80

£796.97

1.5T excavator; incl. insurance + fuel allowance

Supply £10 each)

Wall cabinet

12.5mm standard gyproc

18.90

£60.30

648.00

£27.22

Mirror

£45.50

£59.10

adhesive and grout

Plasterboard to stud wall - outer

timber

Material removed from site

£102.59

5m

Mid spec (Howdens)

plasterboard

undergrowth in G | Ground Floor

1point

Mist coat and two coats of eggshell

£306.52

330.00

Mid spec (Hamilton, PC

£52.93

softwood architrave

Mid spec (Dulux or similar approved)

30.24m²

External wall insulation / External

Mid spec (PC Sum £60/m2)

to skips

3,006.00

Supply £10 each)

£482.09

45m²

45m²

£60.31

Skim to ceiling

Specification

Shower screen

£899.55

Page 35 of 48

£80.15

£85.54

Specification

3mm thistle multi-finish

£392.06

£497.81

Page 36 of 48

475.20

£177.28

28m³

2point

paint to ceiling

Page 28 of 48

£0.00

6.00

£1,687.50

£13.20

leaf in Middle Floor

Qty

£1,231.12

£73.51

Primer, undercoat and gloss coat to

£0.00

Labour

Ceramic tiles to walls, excluding

£482.09

Qty

Wall hung sink

Paint to windows

£120.63

£1,188.00

£121.20

Mid spec (Dulux or similar approved)

12.5mm standard gyproc

Wall Board

48.00

100mm Kingspan Kooltherm Insulation K15 Rainscreen Board

Labour

Specification

Materials

£2,875.50

plasterboard

Page 38 of 48

£26.40

£298.48

7.70

£497.81

£0.00

Mid spec (The Bath Store, PC Supply £140)

Skim to walls

1,044.00

Steel column in G | Ground Floor

30.24m²

Timber stud wall / timber partition

Total

Mist coat and two coats of eggshell

176.40

Materials

Qty

£1,231.12

window

adhesive and grout

Page 19 of 48

£147.02

Wood sheathing to roof in R |

£177.28

Mid spec (PC Sum £60/m2)

Labour

Page 26 of 48

Hardcore

Mid spec (Dulux or similar approved)

Total

wall; 600mm centres; 3 rows of

203x203x86 UC

3mm thistle multi-finish

7.78

760.32

Pitched roof

First Fix Pipework

£121.20

Materials

Specification

paint to ceiling

14.40

Wall mounted sink tap and mixer

Inset mirror in WC

10.8m

Total

noggins in G | Ground Floor

Page 41 of 48

Page 46 of 48

Shower screen in Bathroom

18mm Structural Hardwood

Mid spec (Dulux or similar approved)

£417.20

£298.48

Mid spec (Grohe PC Supply £270)

First fix pipework

Qty

Mid spec (PC Supply £150

13.13

Primer, undercoat and gloss coat

£2,918.98

21.38

each)

Labour

Mid spec (Victoria Plum)

Page 31 of 48

Plywood Sheet

356.40

Skim to walls

Timber stud wall; C16/C24

£3,336.18

47x95mm; 600mm centres;

3mm thistle multi-finish

Materials

1 unit

Mist coat and two coats of eggshell

1 unit

58.499996m²

Total

Page 21 of 48

to window board in Bathroom

17.28

Waste pipe overground

£62.50

Floor board

£614.25

£30.00

3 rows of noggins

£800.28

Hardcore fill / sub base / sub-base

£198.00

Mid spec (Dulux or similar

paint to walls

18mm Structural Hardwood Plywood Sheet

110mm UPVC pipe

£190.80

30.24m²

£719.71

approved)

£228.00

£1,414.53

Mid spec (Dulux or similar approved)

615.60

£253.30

Skim to walls

32.40

51.32

Page 40 of 48

Shower waste

1m

Page 33 of 48

£444.89

3mm thistle multi-finish

in G | Ground Floor

Flooring underlay

28.80

£7.54

Waste pipe overground

Specification

£1,164.60

250mm MOT type 1

Mist coat and two coats of eggshell

£1.20

hardcore

Insulation between studs in G |

Qty

110mm UPVC pipe

Mid spec (Wickes Wood Fibre Underlay or similar approved)

paint to walls

Labour

36.00

Skim to walls

44.79

£8.74

45m²

Ground Floor

Materials

3mm thistle multi-finish

Primer, undercoat and gloss coat

Mid spec (Dulux or similar approved)

£358.03

Flooring underlay

Waste pipe overground

£1,552.50

Total

85.54

46.08

100mm Rockwool RWA45

to window in Bathroom

Semi-Rigid Acoustic

Mid spec (Wickes Wood Fibre Underlay or similar approved)

110mm UPVC pipe

£1,910.53

Shower waste (acrylic tray) in

Page 20 of 48

Mid spec (Dulux or similar

113.76

Pedestal sink

144.00

Insulation Slab

Skim to walls

Bathroom

30.24m²

approved)

3mm thistle multi-finish

Mid spec (Victoria Plum)

74.88

Flush plate

Mid spec (Victoria Plum)

83.99

Waste pipe overground

£284.92

1 unit

1 unit

Mid spec (Grohe PC Supply £85)

110mm UPVC pipe

£131.91

£235.87

Page 44 of 48

£520.79

£50.00

Pedestal toilet

112.20

162.00

£14.40

Page 42 of 48

Weak mix concrete between cavity

Plasterboard to stud wall - outer

£29.99

£146.31

Mid spec (Victoria Plum or similar, PC Supply £190 each)

£79.99

Page 7 of 48

below DPC / Lean mix concrete

250.80

Page 5 of 48

leaf in G | Ground Floor

12.5mm standard gyproc

Perimeter insulation / Insulation to

between cavity below DPC

plasterboard

Weak mix concrete between cavity below DPC; 100mm thick cavity;

25mm thick Kingspan Kooltherm K103 Floorboard to perimeter; n.e.

500mm height allowance

143.47

30.24m²

£177.28

258.72

Page 43 of 48

£121.20

Page 45 of 48

£298.48

Page 22 of 48